## Slide 1
Soubhik Baral
Chaitanya P. Umbare
Jeevitha L
Nidhi Jain
Establishment of Private Wireless Network Using open source Magma Software
05.05.2023

## Slide 2
Agenda
Need of Private Network using Magma Open-Source software
Magma Architecture
Magma Control , Data and Management plane
Magma software components
Magma software components Deployment
Test Bed
  Hardware details
  Test bed configuration
  Lab Set up
Test cases and Results
Application
Future work

## Slide 3
Objective:
Establishment of 4G/5G Transport Network using CBRS eNodeB & Magma Core Network for Helium Hotspot Miner Applications
Need of Private Network using Magma Open-Source software:
To provide reliable, scalable network and Cost effective Solution
Independent of underlying radio technology and spectrum (4G/5G/WiFi)
To address the challenges of rural internet access
Compatible with existing 3GPP network
Stores configuration state centrally and runtime state at the edges.

## Slide 4
Magma Architecture for 4G/5G Cellular Data Coverage
SGW : Serving Gateway
PGW : PDN Gateway
MME : Mobility Management Entity
MSC : Mobile Switching Center
HSS : Home Subscriber Server
PCRF : Policy and Charging Rules Function Server
OCS : Online Charging System

## Slide 5
Management,Control and Data plane

## Slide 6: Magma software components
1.Access Gateway (AGW)

## Slide 7: Magma software components
2. Orchestrator(OR8Cr)

## Slide 8
3. Federation Gateway (FGW)
The FGW integrates Mobile Network Operator (MNO) with magma.
Core functionalities such as authentication, data plans, Policy enforcement , charging should be uniform.
FGW is proxy : one side, it speaks with protocols (s6a,SGs..)
other it side GRPC

## Slide 9: Magma software components Deployment
Access Gateway (AGW) was deployed using Vagrant
Orchestrator(ORC8r) was deployed using docker and its container was registered in docker hub account
Federation Gateway (FGW) can also be deployed using docker.

## Slide 10: Test Bed Hardware Details
Customer Premise Equipment (CPE)
  Baicells Atom ID06G
  SIM card
4G Base station
  Baicells Neutrino 430 eNB
Magma Access Gateway and Orchestrator deployment
  KU551 development kit based on i-7 processor
Application Client / Server
  Intel x86 based system

## Slide 11: Test Bed Configuration
eNodeB
  Band 48 - TDD
  3GPP Rel. 15
Subframe Assignment
  DSUDD
  MIMO – 2x2
  Bandwidth – 20 MHz
Magma
  AGW
  ORC8r

## Slide 12
Lab setup of 4G/5G LTE Private Network over CBRS band using Magma Software components

## Slide 13: Test Cases & Results
Throughput
  DL ~ 110 Mbps
  UL ~ 15 Mbps
VoIP Call
  Using Open Source Asterisk SIP Server & Client

## Slide 14
Application: Helium Hotspot Miner for 4G/5G Coverage
IoT Sensor Nodes
Helium Hotspot Miner/Gateway
Data Packet Forwarder
(Over LoRa)
Cellular Data Forwarder
(Over 4G/5G coverage)
Helium Miner Docker
Magma
Access Gateway
UE
CBRS Cell
CBRS Band
Orchestrator
Helium Network Server
Internet
Magma
Federation Gateway
Mgmt+ Relay
Mgmt+ Relay

## Slide 15: Future Work
Integration & Testing of Magma 5GCN with 5G gNodeB/CPEs
Scale the Network with Multiple AGW, Base station
Deployment of orchestrator in cloud instead of ku551
Integration of Federation Gateway to the network.

## Slide 16
THANK YOU